## Slide 2
C-ITS AND TOLL FREQUENCY THREATS
Manfred Haase
ASFINAG Maut Service GmbH
manfred.haase@asfinag.at

## Slide 3: Agenda
The whole story of interference
What is interference?
What means interference for electronic tolling?
Who is interfering with electronic tolling?
Interference mitigation measures

## Slide 4: What Is Interference?
Interference: Effect of unwanted energy upon reception
No exclusive usage of tolling frequency band
Interference cannot be completely avoided
Interferer avoids interference when “listening” before “talking”
Interferer
Receiver
Sender
Interference is unwanted energy perceived by the receiver:
Notes: Interference is the effect of unwanted energy upon reception in a radio communication system.
There is no exclusive usage of the tolling frequency band
This means: interference cannot be completely avoided. The regulation assumes protection distances or requires mitigation techniques.
Incumbent applications are normally protected.
The regulation for road tolling systems is very old. However, „short range devices“ have even older rights.
New radio applications have to demonstrate that the incumbents don‘t get interfered. For that reason, CEPT performs compatibility studies.

## Slide 5: What means interference for electronic tolling?

## Slide 6: Toll Transaction – without interference
Toll RSU
Toll OBU
RSU to all: is there anybody?
OBU to RSU: here is OBU #7
RSU to OBU#7: Your data please
OBU #7 to RSU: Here are the data
RSU to OBU#7: Confirmation
OBU #7 to RSU: Ok.
RSU to OBU#7: End.
RSU to all: is there anybody?
…
Communication Zone
RSU constantly asks for OBUs

## Slide 7: Toll Transaction – with short-term interference
Toll RSU
Toll OBU
RSU to all: is there anybody?
OBU to RSU: here is OBU #7
RSU to OBU#7: Your data please
OBU #7 to RSU: Here is the Data
RSU to OBU#7: Confirmation
OBU #7 to RSU: Ok.
RSU to OBU#7: End.
RSU to all: is there anybody?
…
RSU to OBU#7: Your data please
OBU #7 to RSU: Here are the data
#!$%&/]! Interfering signal
Repetition only possible until the vehicle leaves the communication zone!
Communication Zone
Repeated
Repeated
short-term interference

## Slide 8: Toll Transaction – with long-term interference
Toll RSU
Toll OBU
RSU to all: is there anybody?
OBU: I can‘t understand anything
RSU to all: is there anybody?
…
RSU to all: is there anybody?
RSU to all: is there anybody?
Communication zone
long-term interference
 No toll transaction
#!$%&/]!
&&%$§(
&%$/()((
$$%³%%&
&&%%&&
Interfering signal
 Revenue lost!

## Slide 9: Who is interfering with electronic tolling?

## Slide 10: Possible interferers
W
Toll RSU
CEN DSRC
C-ITS RSU
Toll OBU
CEN DSRC
C-ITS
OBU
W
RLAN
(e.g. Wi-Fi)
Urban Rail ITS
(CBTC)
Smart Tachograph
WIA
Generic Short Range Devices (SRDs)
Fixed Wireless Access
Wi-Fi in vehicles
Mil. Radars
Amateur Radio
C-ITS
OBU
W
Toll communication zone (approx. 10m)
Interference zone depending on transmission power of the interferer and attenuation
W
W
Wi-Fi in vehicles

## Slide 11: Usage of The 5-GHz frequency band
WiFi channels and frequency
 No problems
 Potential problems
 Problems expected
Toll systems
WiFi
(WLAN)
C-ITS
Short Range Devices
(SRDs)

## Slide 12: Use of The 5.8-GHz frequency band
There are more and more users around the tolling frequency at 5.8 GHz.
The tolling protocol can compensate short term interference, but not extensive interference.
Once interference becomes visible in toll transaction statistics, it is too late! The interferers are already on the market and in the field.
Interference has a negative impact on revenue situation of toll chargers and toll service providers
Therefore: active cooperation in European frequency regulation and standardization, in order to prevent and avoid problems
Interference costs money!
Notes: The frequency band around the tolling frequency at 5.8 GHz is becoming used more and more.
Potential negative impact on profit situation of toll chargers:
  Compare revenue and success rate
  Local short-term interference in individual toll stations might be partially corrected by the tolling protocol
  Extensive interferences lead to a decrease of the success rate.
Interferences will only be discovered if the robustness mechanism in the toll system doesn‘t work anymore. But at this point it is too late as the interfering systems are already on the market and in the field.
Developments of the frequency regulation and standardisation in this area has to be followed.
Therefore: active cooperation in CEPT, ETSI and CEN, in order to prevent and avoid problems

## Slide 13: Interference mitigation measures

## Slide 14: Why do we need mitigation measures?
Older rights count
  incumbent radio applications are normally protected
  Short range devices (SRD) even older rights than tolling systems
New rights lead to (potential) problems
  More transmission power
  New frequency bands
  New technologies
  More frequent transmissions
  Not “listening” before “talking”
Notes: The frequency band around the tolling frequency at 5.8 GHz is becoming used more and more.
Potential negative impact on profit situation of toll chargers:
  Compare revenue and success rate
  Local short-term interference in individual toll stations might be partially corrected by the tolling protocol
  Extensive interferences lead to a decrease of the success rate.
Interferences will only be discovered if the robustness mechanism in the toll system doesn‘t work anymore. But at this point it is too late as the interfering systems are already on the market and in the field.
Developments of the frequency regulation and standardisation in this area has to be followed.
Therefore: active cooperation in CEPT, ETSI and CEN, in order to prevent and avoid problems

## Slide 15: Who influences the use of frequency bands?
Legal acts based on CEPT decisions
CEPT Reports,
ECC Decisions
Frequency regulation
(compatibility studies and decisions)
Referencing of Harmonised Standards in Official Journal of the EU ( CE marking)
European Telecommunications Standards Institute
Harmonised Standards
(conformity with the frequency regulation)
Decision makers: mainly industry
Implementation in national
regulations
Decision makers: radio authority
 ASCEAP observer in ECC
 ETSI/CEN standardization
 EU consultations

## Slide 16: ASECAP Protected Zone Database
Database with protected zones will be installed by OEMs in vehicles
C-ITS
PZDB
Vehicles reduce transmission power and transmission frequency (Duty Cycle) in the protected zone while driving

## Slide 17: ASECAP Protected Zone Database
Database with protected zones around toll stations
C-ITS equipped vehicles use the PZDB and mitigate interference in protected zones
Other radio applications can use it as well
Continuous updates of the PZDB is important
  by ASECAP members,
  in the vehicles by the OEMs
Widespread use of the PZDB is important
PZDB
Successfully used in
vehicles today!
Notes: Database with protected zones around toll stations
Interference mitigation in protected zone mitigation techniques are to be used
Mitigation in protected zones is mandatory for ITS equipment.
Other radio applications can use the ASECAP protected zone database as well (WiFi, Wireless Industrial Applications, etc.)
Essential advantage: protected zones are just a small part of the land area of a country – thus the impact on other radio applications is small
Frequency regulation (CEPT) and standardisation (ETSI) have been made aware of the database.

## Slide 18: Takeaways
The tolling frequency is not exclusive
  Tolling frequency is mandated in EU legal acts
  Interferences must be expected
  „The stronger (transmission power), the more frequent and the closer (distance, frequency), the worse“
  Interference into toll systems costs money
Biggest threats
  5G-V2X and LTE-V2X (2x more frequent transmissions)
  Non-compliant equipment
  Non-compliant use of equipment (indoor/outdoor)
Mitigation
  Active participation in frequency regulation (CEPT), standardization (ETSI, CEN) and EU consultations
  ASECAP protected zone database must be used

## Slide 19
INSERT CONTACT DETAILS